## Slide 1: Isolation and Protection in Operating Systems 4. Paging in x86-64
Prof. Dr. Michael Schöttner
Dr. Fabian Ruhland

## Slide 2: Current State
We use segmentation to differentiate between kernel and user code
  User mode threads cannot execute privileged CPU instruction
  We also blocked accesses to I/O-ports for user mode threads via the TSS
We now implement paging to restrict memory accesses
  This enables us to isolate user mode processes...
  ...and protect the kernel’s memory area from being accessed by user mode code

## Slide 3: Paging
Virtual address space is divided into equal sized pages
Virtual address space is divided into equal sized page frames
Usually 4 KiB pages and thus 4 KiB page frames are used
  One page frame stores exactly one page
  Special case: Huge Pages, e.g. 2 MiB or 1 GiB
Memory protection can be specified with a 4 KiB granularity
  Read only
  Execute
  User mode access allowed/forbidden

## Slide 4: Virtual vs. Physical Addresses
Virtual/Logical addressesare differentiated from physical addresses
  Virtual addresses use up to 57 bit, depending on the CPU
  Addressable physical memory depends on the installed DRAM
  A block of virtual memory can be mapped to arbitrary page frames
A
B
C
B
C
A
Virtual Address Space
Physical Address Space
Page Table
...
4
3
2
1
0
...
...
...
2
0
4
#Page
#PF
#Page 0 1 2 3 4
0 1 2 3 4 #Page-Frame (=PF)

## Slide 5: Process Isolation
Each process has its own page tables describing its virtual address space
We map the kernel memory into every address space
Kernel Space
User Space 2
Process 2
Page Tables for Process 1
User-Space 1
Kernel-Space
Page Tables for Process 2
User-Space 2
Kernel-Space
Kernel Space
User Space 1
Process 1
Physical Address Space
available
Page frames can be mapped arbitrarily

## Slide 6: Process Isolation
Each thread runs in a process address space and can only access virtual addresses on pages that are allowed by the corresponding page table entries
This is controlled by bits in the page table entries (see next slides)
If a page is not present, it is either swapped out or unused
  Accessing it causes a Page Fault
The page tables themselves must be protected from user space accesses (just like the kernel)
  This is controlled by a specific bit in the page table entries (see next slides)

## Slide 7: Long Mode: Segmentation
16-bit selectors
Start addresses are ignored (except FS and GS)
  FS: For thread-local storage (used by thread libraries)
  GS: Linux uses it to retrieve the stack address for fast system calls
No limit checks
  Only the ring number in CS remains relevant

## Slide 8: Long Mode: Paging
Paging is mandatory in Long Mode
The basic paging configuration is handled by the CRx Control Registers
Picture: Horst Schiermeier, TU Dresden
Physikalische Adresse

## Slide 9: Long Mode: Page Tables
Picture:James Mickens, Harvard
Four level Paging
  Modern CPUs may support five levels
Index: 9 Bit
  4 KiB per table
  8 byte per entry
  512 entries per table

## Slide 10: Page Table Entry
Picture: Horst Schirmeier, TU Dresden
Configuration is possible on all level of the page table hierarchy
Protection bits:
  R/W = Read/Write → Protection agains write accesses
  NX = NoeXecute → Prohibit code execution in memory that only contains data
  U/S = User/Supervisor → Access allowed for everyone or only in ring 0
  Available = AVL = Bits that are freely usable by the operating system

## Slide 11: Bemerkungen
Warum gibt es so viele Stufen?
  I.d.R. wird der virtuelle Adressraum nur spärlich und verstreut genutzt
  Allenfalls großer Heap bei Big-Data-Systemen
  Aber Stacks und Code benötigen nicht Gigabytes
Es werden nur notwendige Tabellen angelegt
  Ein Eintrag in PML4E beschreibt 512 GB
  Falls dieser Adressbereich komplett ungenutzt ist, so wird PML4E.present bit = 0 gesetzt
  Und entsprechend werden nicht alle zugehörigen Tabellen PDP/PD/PT Tabellen in diesem Unterbaum angelegt

## Slide 12: Example: 1 GiB Pages
Picture: James Mickens, Harvard

## Slide 13: Example: 1 GiB Pages
Picture: James Mickens, Harvard

## Slide 14: Long Mode: TLB
Problem: Paging requires address translation by the Memory Management Unit (MMU) → One MMU per core
  Address translation is slow because of the four/five levels of page tables
  Long Mode requires paging
Solution: Translation Lookaside Buffer (TLB) → One TLB per core:
  Buffers translated addresses
  Fully associative cache → Lookup in O(1)
    Tag: consists of page table indices
    Data: page frame address

## Slide 15: Long Mode: TLB
Picture: James Mickens, Harvard

## Slide 16: Long Mode: TLB
Picture: James Mickens, Harvard

## Slide 17: Long Mode: TLB
Before raising page fault exception, HW sets cr2 to faulting address, and pushes an error code onto stack
Ex1: User thread tried to read a non-present page
Ex2: User thread tried to write a present but read-only page
Picture: James Mickens, Harvard

## Slide 18: Long Mode: TLB
TLB is small: ~32-100 entries (depending on the CPU)
In usual application the TLB reaches a hit rate of up to 98%
  Why? → Principle of locality
  Arrays, Loops, etc.
Remarks
  Writing the CR3 register (address space switch) fully invalidates the TLB
  Whenever protection/access bits in a page table are modified, the corresponding TLB entry must be invalidated manually (INVLPG instruction)
    On multicore CPUs, this may be necessary on all cores!

## Slide 19: To Be Continued...
Kernel isolation after Meltdown
Process Context Identifiers
Memory protection keys