## Slide 1: OS Development 3. Programming model of the x86_64 processor architecture
Prof. Dr. Michael Schöttner
Dr. Fabian Ruhland

## Slide 2: Preview
History
x86 programming model
Address translation
Protection
Tasks
Summary

## Slide 3: History
Advanced Vector Extensions (based on SSE)
Transactional Synchronozation Extensions
Fuse-Multiply-Add Instructions
Deep-Learning (DL) Boost → AVX extension
P = Performance E = Efficiency Hybrid Cores
8086 (1978) - Prime father of the PC processor
80286 (1982) - Segmentation based memory protection
80386 (1985) - Paging → Memory protection based on pages
Pentium (1993) - superscalar, 64-bit data bus, MMX, APIC
Pentium II (1997) - RISC-like micro instructions
Pentium III (1999) - SSE
Pentium 4 (2000) - SSE2, Hyperthreading, Intel 64 / EM64T
Core (2005) - Dual Core
Core 2 (2006) - Quad Core, 64 bit (x86_64)
Has-/Broad-well (2013) - AVX2, TSX, FMA3
Rocket / Tiger Lake (2021) - DL-Boost, Memory encryption
Alder Lake (2021) - Division in P- and E-cores (max. 8 + 8)
3.1 History

## Slide 4: Preview
History
x86 programming model
Address translation
Protection
Tasks
Summary

## Slide 5: 8086
16-bit architecture, little endian
20-bit address bus → 1 MiB max. physical memory
Few registers (from todays standpoint)
123 instructions (1-4 byte length)
Segmented memory (64 KiB segments)
Stil relevant today
  On multicore systems, other cores startup in real moe
3.2 x86 programming model

## Slide 6: 8086: Registers
3.2 x86 programming model
Picture based on: Volkmar Sieh / Daniel Lohmann, University Erlangen

## Slide 7: 8086: Registers
Picture based on: Volkmar Sieh / Daniel Lohmann, University Erlangen
3.2 x86 programming model

## Slide 8: 8086: Segmented Memory
Logical addresses consist of:
  Segment selector (determined by a segment register)
  Offset (usually given by a general purpose register or directly encoded into the instruction)
  Physical address calculation:
3.2 x86 programming model
Picture based on: Volkmar Sieh / Daniel Lohmann, University Erlangen

## Slide 9: 8086: Segmented Memory
640K ought to be enough for anybody.
3.2 x86 programming model

## Slide 10: 8086: I/O-Port vs. Memory Addresses
I/O-port and memory addresses:
  Differentiation through CPU pin M/IO.
  16 address lanes for I/O → 16-bit
  Still supported today (even in Protected Mode and Long Mode)
Additionally: Memory Mapped I/O (e.g., for video cards)
  Memory access goes to a device instead of memory
3.2 x86 programming model

## Slide 11: IA-32 – The 32-bit Intel Architecture
First IA-32 CPU was the Intel 80386
  The term IA-32 was introduced much later
32-bit technology: register, data und address bus
  From Pentium Pro: 64 Bit data und 36 bit address bus
Complex protection and multitasking support
  Protected Mode
  Originally introduced with the 80286 (16-Bit)
Compatibility
  With older operating systems through Real Mode
  With older applications through Virtual 8086 Mode
Segmentation based memory model (mostly used as Flat Memory)
Page based Memory Management Unit (MMU)
3.2 x86 programming model

## Slide 12: x86-64: 64-bit CPU Architecture
x86-64: Original name of 64 bit extension by AMD
  Sometimes abbreviated as x64
  Later replaced by AMD64
Intel licensed x86-64 from AMD
Intel 64 is Intel’s own label (for the same architecture)
  Minimal differences in instruction set compared to AMD64
  Completely different than the own IA-64 (Itanium) architechture
3.2 x86 programming model

## Slide 13: x86-64: 64-bit CPU Architecture
Additional registers (all 64 bit long)
Paging must be enabled
Segmentation strongly restricted
New feature (among others): No Execute protection per page
3.2 x86 programming model

## Slide 14: x86-64: CPU modes
Real Mode = 16 bit addressing
Protected Mode = 32 bit addressing (also called IA-32)
Long Mode = 64 Bit addressing (also called IA-32e)
  e meaning extension
  Used in the Intel manuals
  To differentiate against IA-64
(Compatibility Mode)
  Supporting Protected Mode applications in Long Mode
3.2 x86 programming model

## Slide 15: x86-64: Registers
Picture: Horst Schirmeier, TU Dresden
3.2 x86 programming model

## Slide 16: x86-64: Registers
Picture: Horst Schirmeier, TU Dresden
3.2 x86 programming model

## Slide 17: Preview
History
x86 programming model
Address translation
Protection
Tasks
Summary

## Slide 18: x86-64: Addressing
Picture: Horst Schirmeier, TU Dresden
Effective addresses (EA) are calculated using the following scheme
  All general purpose registers can be used
Example: MOV RAX, array[RSI * 4]
  Lesen aus einem Array mit 4 Byte großen Elementen und RSI als Index
New in x86-64: Addressing relative to instruction pointer

## Slide 19: Protected Mode – Segments
Each segment has a start address and a length
Segment registers store segment selectors = Index into the GDT/LDT
  LDT was rarely used by operating systems
A program (in execution) consists of multiple memory segments
  At least CODE, DATA and STACK
Linear address is segment start address + effective address
  Effective address = Value in a general purpose register
  Linear address = physical address, if the paging unit is turned off
3.3 Address Translation

## Slide 20: Protected Mode – Segments
Flat memory:
  Practically all modern 32-bit operating systems set all segments to start address 0
  This way, segments do not influence address calculation
  Furthermore, only four GDT entry are used (CODE + DATA, each for User and Kernel Mode); LDT remains completely unused
Segmentation cannot be turned off (because of protection), but Paging is not required in IA-32 Protected Mode
3.3 Address Translation

## Slide 21: Protected Mode – Segments
Picture based on: Volkmar Sieh / Daniel Lohmann, University Erlangen
3.3 Address Translation

## Slide 22: Long Mode: Segmentation
16-bit Selectors
Start addresses are ignored in almost all segments, except FS and GS
No limit check; essentially only the ring number in CS remains relevant (= CPL)
3.3 Address Translation

## Slide 23: Long Mode: Paging
Paging is mandatory in Long Mode
The basic paging configuration is handled by the CRx Control Registers
Picture: Horst Schiermeier, TU Dresden
Physical Address
3.3 Address Translation

## Slide 24: Long Mode: Page Tables
Four or five levels of page tables
3.3 Address Translation
Picture: Horst Schiermeier, TU Dresden

## Slide 25: Long Mode: TLB
Problem: Paging slows down memory accesses, since the page tables need to be accessed each time
Solution: Translation Lookaside Buffer (TLB):
  Fully associative cache
  Tag: consists of page table indices
  Data: Page Frame address
  Size (80386): 32 entries
With normal applications, the TlB reaches a hit rate of ~98%
Remarks:
  Writing the CR3 register invalidates the TLB
    Not anymore since Intel Westmere (2010) → TLB Tag has additional 12-bit Process Context ID (PCID)
  When protection/access bits in a page table entry are modifired, the corresponding TLB entry must be deleted (INVLPG instruction)
3.3 Address Translation

## Slide 26: Preview
History
x86 programming model
Address translation
Protection
Tasks
Summary

## Slide 27: Protection
Goals:
  Protection against unauthorized memory accesses and code execution
  Protection against kernel crashes or crashes of other processes
Requirements: Coda and Data...
  are classified in regard to their trustability
  and this classification is enforce by the operating system, with the help of the process

## Slide 28: Protection Rings
Each segment descriptor (Code/Data) has two bits, determining which privilege level the segment is assigned to
  Up to four privilege levels possible
  In practice, only two are used
0
1
2
3
Daten
Code
Daten
Daten
Daten
Code
Code
Code

## Slide 29: Protection Rings
Smaller ring numbers grant more privileges
Ring 3 is meant for applications
  = User Mode
Ring 0 is meant for the OS
  = Kernel/Supervisor Mode
0
1
2
3
Application
OS

## Slide 30: Protection Rings and Gates
Accessing memory of an inner ring is forbidden and such accesses are prohibited by the MMU
  General Protection Fault
Code of an inner ring can only be called via Gates
  Allow direct calls from ring 3 to ring 0
Memory accesses and calls to outer rings are always allowed
0
1
2
3
Gate

## Slide 31: Segment Descriptors
Are entries in the Global Descriptor Table (GDT) and allow code protection
  (IA-32: additional protection via limit (= end of segment))
  8 byte per entry (Exception: system segments use 16 byte in x86_64)
Picture: Volkmar Sieh / Daniel Lohmann, University Erlangen
TYPE
Code/Data
Read/Write
Non-/Conforming
System Segments (Call-Gate, Task State Segment)

## Slide 32: Flat Memory Model
Picture: Horst Schirmeier, TU Dresden
Most 32-bit PC operating systems have not used segmentation
  32-bit effective address = linear address
In Long Mode (64 bit) the segment base address is ignored by the processor
Protection via Paging:
Each process only sees its own virtual address space
  Page level access control (see next slides)

## Slide 33: Page Table Entry
Picture: Horst Schirmeier, TU Dresden
Flags are settable on all levels of the page table hierarchy
Protection bits:
  R/W = Read/Write → Protection agains write accesses
  NX = No eXecute → Do not execute code inside data
  U/S = User/Supervisor → Access allowed for all or only in ring 0
  Available = AVL = These bits are free to use by the operating system

## Slide 34: x86_64: Summary - Protection
Modern 64-bit operating systems only need the followin GDT entries
  One data segment descriptor
  Two code segment descriptors (one with DPL = 0 and one with DPL = 3)
Protection is enforced via Paging
  Protection bits (NX, U/S, R/W)
  Page Tables:
    Which pages are present/accessible?

## Slide 35: Preview
History
x86 programming model
Address translation
Protection
Tasks
Summary

## Slide 36: IA-32: HW Support for Multitasking
State of a task is stored in a Task State Segment (TSS)
  Stores all registers
  Stack pointer for each ring
  CR3 register
  I/O permission bitmap (see next slides)
Current TSS determined by Task Register (TR) of a CPU core
  Each core has its own TR
Task switch with hardware support via a Task Gate
  Not used in most operating systems and instead implemented in software
3.5 Tasks

## Slide 37: Long Mode: Multitasking
No HW support for task switching
TSS existent, but only stores:
  Stack pointer per ring
  IST = Interrupt Stack Table
  I/O permission bitmap (see next slide)
IST allows separate stacks for interrupt handlers
  IST number can be specified in entries inside the Interrupt-Descriptor Table (IDT)
Picture: Horst Schirmeier, TU Dresden
3.5 Tasks

## Slide 38: Long Mode: I/O Permission Bitmap
Access protection for I/O-ports (only little relevance nowadays)
  I/O privilege level (IOPL) represented by two bits inside the RFLAGS register
  Port access is granted if CPL ≤ IOPL
  Otherwise, the I/O permission bitmap is used
    One bit for each port; if a bit is set, access is denied
Access protection for memory mapped I/O via page tables
Picture: Horst Schirmeier, TU Dresden
3.5 Tasks

## Slide 39: Preview
History
x86 programming model
Address translation
Protection
Tasks
Summary

## Slide 40: Summary
x86-64 architecture is highly complex
  Virtual memory with four or five level paging
  Page based memory protection
  I/O-port access protection per task
  Can execute 16-bit code in IA-32 Protected Mode or 32-bit code in Long Mode
Rarely used features were removed
  Segmentation (mostly)
  Hardware support for task switching
Still backwards compatible
  Processor and cores still start up in Real Mode
3.6 Summary

## Slide 41: More Features
Virtualization
  Virtual 8086 Mode
    16-bit application
  Intel-VT, AMD-V
    HW support for VMware, VirtualBox, etc.
    Hypervisor runs in ring -1
AVX: Advanced Vector Extensions
TSX: Transactional Synchronozation Extensions
Hybrid Cores
3.6 Summary