## Slide 1: OS Development 4. Interrupts
Prof. Dr. Michael Schöttner
Dr. Fabian Ruhland

## Slide 2: Preview
Basics
Interrupt Handling in x86_64
Programmable Interrupt Controller
Advanced Programmable Interrupt Controller
Interrupt Handling in Operating Systems
Summary

## Slide 3: 4.1 Basics
Interrupts were introduced, to allow overlapping execution of input/output operations
Instead of actively waiting for an I/O-operation to end, the affected thread is blocked and another thread is executed → This way, the CPU is used in a meaningful way
Furthermore, interrupts form the basis of preemptive multithreading
  Programme Interval Timer (PIT) generates periodic interrupts (see PC Speaker)
  Preemtpive multithreading is discussed (and implemented) later
4.1 Basics

## Slide 4: Interrupt Hardware: Single Core
Picture: Volkmar Sieh / Daniel Lohmann, University Erlangen
4.1 Basics

## Slide 5: Priorization
Background
  Multiple interrupts may be signaled at the same time → Which one is more important?
  While the CPU is handling an interrupt, further interrupts may be signaled
Priorization mechanism
  In software: The CPU only has a single IRQ (interrupt request) input
  In hardware: A priorization circuit assigns a priority to each device and only forwards the most important IRQ to the CPU
  Modern interrupt controllers allow dynamic priorities
4.1 Basics

## Slide 6: Assignment of Interrupt Handlers
Problem:
  Software should know which device has triggered an interrupt as fast as possible
    We do not want to ask all devices manually
Solution: Interrupt Vector
  Assign a unique vector number to each interupt, that is used as an index into a vector table
    The vector number does not necessarily correlate with its priority
    In practice, multiple device might have to share the same vector number (Shared Interrupts)
  Structure of the interrupt vector table depends on the CPU architecture
    Oftentimes only contains function pointers
4.1 Basics

## Slide 7: Storing the System State
Problem:
  After executing an interrupt handler, the CPU must return to the thread context
  The interrupt handler should be "slid in" unnoticed
Solution: Store the system state
  By Hardware:
    Only the essentials: e.g. return address and flags register
    Restoring is done via a special instriction (e.g, iret, ...)
  By Software:
    Because interrupts may occur any time, the handler must store and restore all registers it uses
4.1 Basics

## Slide 8: Nested Interrupts
Problem:
  To handle important events as fast as possible, interrupt handlers should also be interruptible
  Infinite nesting depth must be avoided
Solution:
  The CPU only allows interrupts with a higher priority
  Rarely implemented, since it introduces complexity and is usually not needed in practice
4.1 Basics

## Slide 9: Multicore Systems
Problems:
  Which core handles an interrupt?
  Handling inter-processor interrupts (IPI)
Solution: Additional hardware for interrupt handling
  Routing interrrupts to CPU cores is controllable via software
  Fixed or random assignment
  Assignment with respect to the thread priorities on the respective CPU core
4.1 Basics

## Slide 10: Interrupt Hardware: Multicore
Picture: Volkmar Sieh / Daniel Lohmann, University Erlangen
4.1 Basics

## Slide 11: Danger: Spurious Interrupts
Problem: Wrong interrupt request, because of
  Hardware faults
  Incorrectly programmed devices
Solution:
  Avoid hard- and software errors
  "Defensive" programming in operating systems
    Expect spurious interrupts
4.1 Basics

## Slide 12: Danger: Interrupt Storms
Problem:
  Highly frequent interrupt request can paralyze an operating system
  Either caused by real interrupts, or the CPU is unable to cope with the I/O-load
  Can easily be confused with Page Thrashing
Solution (in the operating system):
  Detect interrupt storms
  Deactivate the affected device
4.1 Basics

## Slide 13: Preview
Basics
Interrupt Handling in x86_64
Programmable Interrupt Controller
Advanced Programmable Interrupt Controller
Interrupt Handling in Operating Systems
Summary

## Slide 14: External vs. Internal Interrupts
External/Hardware interrupts
  Triggered by a device (e.g., timer)
  Come from the outside (from the CPU’s point of view)
Internal/Software interrupts
  Triggered by the CPU itself
    Exceptions (see next slides)
    Assembly instruction INT <nr>
      Used for System Calls (Linux, Windows NT, MacOS, MSDOS)
4.2 Interrupt Handling in x86_64

## Slide 15: Exceptions
Fault
  Operating system can handle and recover from faults (e.g., Page Fault)
  CPU state and the address of the fault triggering instruction are stored
Trap
  Triggered by a special instruction (e.g., INT 3 - Breakpoint)
  Program can be continued
Abort
  Unrecoverable error
  Triggers are hard to localize exactly
  Cause a reboot (e.g., Double Fault)
4.2 Interrupt Handling in x86_64

## Slide 16: Vectors
Interrupts and exceptions are identified via a Vector Number
0 – 31 are reserved for exceptions
32 – 255 are freely available
Examples for exceptions:
Vector | Exception | Vector | Exception
0 1 2 3 4 5 6 8 | Division by 0 Debug NMI Break Overflow Bounds range exceeded Illegal instruction Double fault | 11 12 13 14 16 18 … | Segment not present Stack overflow General protection fault Page fault - Machine check . . .
4.2 Interrupt Handling in x86_64

## Slide 17: Assigning Handlers to Vectors
Interrupt Descriptor Table (IDT)
IDT start address is stored in IDTR (1 per core)
255 entries map each vector to an address (function pointer)
  This function is the Interrupt Handler / Interrupt Service Routine / ...
  8 byte per entry (either Interrupt Gate or Trap Gate)
Interrupt-Gate: Describes an interrupt handler
  When this entry is used, all interrupts on the CPU core are masked (deactivated) → Interrupt Enable bit in RFLAGS is unset
Trap-Gate: Describes a trap handler
  Works the same as and interrupt gate, but without masking interrupts
  For example used for system calls via software interrupts
4.2 Interrupt Handling in x86_64

## Slide 18: Assigning Handlers to Vectors
Interrupt table entry format in Long Mode
Segment selector is index into the GDT
4.2 Interrupt Handling in x86_64

## Slide 19: Stack Buildup during Interrupts
Program is interrupted after execution of the last instruction
4.2 Interrupt Handling in x86_64

## Slide 20: Stackup Buildup without Ring Change
If the privilege level is not changed, the CPU does not switch the stack
The interrupt handler operates on the stack of the interrupted thread
This happens in HeineOS (all our code runs in ring 0)
Only some exceptions push an error code
RFLAGS
CS
RIP
(error code)
Stack of the interrupted thread
RSP before transferring control to handler
RSP after transferring control to handler
4.2 Interrupt Handling in x86_64

## Slide 21: Stack Buildup with Ring Change
New stack is read from Task State Segment (see last chapter)
RSP
RFLAGS
CS
RIP
(error code)
Handler Stack
RSP after transferring control to handler
Stack of the interrupted thread
RSP before transferring control to handler
SS
4.2 Interrupt Handling in x86_64

## Slide 22: IDT: Typical Example
Entries 0-31 are reserved for x86 CPU exceptions
  Either DPL=0 or DPL=3, depending on use case
Entries for external interrupts
  IRQs have DPL=0
System calls via trap gate (Windows & Linux)
  DPL=3
  Replaced by SYSENTER/SYSEXIT in modern operatings systems → faster, avoids interrupt overhead
Since HeineOS runs completely in ring 0, we do not need trap gates
4.2 Interrupt Handling in x86_64

## Slide 23: System Call via a Trap Gate
4.2 Interrupt Handling in x86_64

## Slide 24: Preview
Basics
Interrupt Handling in x86_64
Programmable Interrupt Controller
Advanced Programmable Interrupt Controller
Interrupt Handling in Operating Systems
Summary

## Slide 25: Interrupts in x86 CPUs
Upto and including the i486 x86 CPUs only had a single input for IRQs
External hardware was tasked with Priorization and vector number generation
  Through a chip alled PIC 8259A
    8 interrupt inputs
    15 input by cascading two PICs
4.3 Programmable Interrupt Controller

## Slide 26: PIC Architecture
Master controller can handle up to 8 slaves (CAS0..2 = Cascade Lines)
In PCs only one slave is used (IRQ2)
4.3 Programmable Interrupt Controller

## Slide 27: PIC Architecture
Typical IRQ assignment in PCs:
Priorities
  IRQ0 has highest priority
  Default IRQ priorities: 0, 1, 8...15, 3... 7 (because of cascading)
  Interrupts with a higher priority can interrupt ones with lower priorities (provided that the IE-bit (=Interrupt Enable) allows interrupts)
IRQ# | Device
0 1 2 8 … 12 … 3 … | Programmable Interval Timer Keyboard Controller Slave PIC Real Time Clock … PS/2 Mouse … COM2 ...
4.3 Programmable Interrupt Controller

## Slide 28: PIC Register
8 bit per register (1 bit per IRQ)
Interrupt Mask Register (IMR)
  Enable/Disable interrupts (0=enable, 1=masked).
Interrupt Request Register (IRR):
  Stores pending interrupts
Priority Resolver:
  Forwards IRQ with highest priority in IRR to ISR
In Service Register (ISR):
  Contains IRQs, that are currently being serviced
4.3 Programmable Interrupt Controller

## Slide 29: Interrupt Flow: PIC <-> CPU
IRQ line is activated → Corresponding bit in IRR is set
PIC sends INTR signal to CPU (slave PIC sends to master PIC instead)
CPU answers with INTA pulse, if IE bit is set in RFLAGS.
Most significant bit in IRR is unset and set in ISR.
CPU sends second INTA pulse
PIC puts vector pointer (8 bit = 3 bit IRQ + 5 bit offset) on data bus.
Interrupt handler sends EOI to PIC when finished → deletes ISR bit
Remark: If interrupt came from slave PIC → also send EOI for IRQ2 to master PIC
EOI not necessary in HeineOS, since we use the PIC’s automatic EOI mode
4.3 Programmable Interrupt Controller

## Slide 30: Interrupt Flow: PIC <-> CPU
Internal interrupts:
  Fixed vector numbers 0 – 31
External interrupts:
  Vector = IRQ + Offset
  Offset > 31 and IRQ != vector
  Offset must map IRQs to vector number > 31
4.3 Programmable Interrupt Controller

## Slide 31: Preview
Basics
Interrupt Handling in x86_64
Programmable Interrupt Controller
Advanced Programmable Interrupt Controller
Interrupt Handling in Operating Systems
Summary

## Slide 32: Advanced Programmable Interrupt Controller
APIC offers more interrupts than PIC and supports multicore and multiprocessor systems
  Interrupts can be distributed to specific cores with respect to thread priorities
  Inter-processor interrupts (IPI) between CPU cores (e.g, for bootstrapping other cores)
  Backwards compatible with PIC (8259)
If existent, the APIC is activated after booting, but runs in PIC compatible mode
  APIC registers are found via Model Specific Registers (MSR)
4.4 Advanced Programmable Interrupt Controller

## Slide 33: APIC Architecture
An APIC interrupt system consists of a Local APIC per core and usually one I/O-APIC (may be more than one)
4.4 Advanced Programmable Interrupt Controller

## Slide 34: Local APIC (per CPU/Core)
Receives interrupt request as messages from the APIC bus
Can additionally process two local interrupts directly
  Via CPU pins: LINT0 and LINT1 (LINT = Local Interrupt)
  Allow backwards compatibility with the PIC
Local APICs are addressable via an ID
Local APICs contain further function units
  Builtin timer (dependent on system bus clock → divisible)
  Interrupt command register
    Used to send APIC messages → Needed for inter-processor interrupts (IPI)
4.4 Advanced Programmable Interrupt Controller

## Slide 35: Interrupt Sources (1)
External device interrupts are signaled by anIO-APIC via the APIC bus
Default behaviour, once the APIC has been activated by the OS
4.4 Advanced Programmable Interrupt Controller

## Slide 36: Interrupt Sources (2)
IPI – Inter-Processor Interrupt
  Generated by another Local APIC → for multicore/multiprocessor systems
  Are sent as messages via the APIC
  For example use to coordinate startup/shutdown, or TLB flush after page tables have been altered
4.4 Advanced Programmable Interrupt Controller

## Slide 37: Interrupt Sources (3)
Local device interrupts:
  Via a CPU pin: LINT0, LINT1 (not via the APIC bus)
  Used for PIC compatibilty mode, if the APIC has note been activated
  Examples:
    Temperature sensor interrupt
    8259A (if existing)
4.4 Advanced Programmable Interrupt Controller

## Slide 38: Local APIC Registers
Task Priority Register (TPR)
  Stores thread priority
  Managed by the OS
Processor Priority Register
  Managed by the CPU
  Results from TPR & ISR
EOI Register
  End-Of-Interrupt
  Must be written before iret
Interrupt Command Register
  For Inter-processor interrupts
4.4 Advanced Programmable Interrupt Controller

## Slide 39: Delivering Interrupts to an APIC
Flat model addressing → Static interrupt delivery
  No arbitration; Delivery to addressed Local APIC; Wait if necessary
Dynamic interrupt delivery
  After determining the group of addressed CPUs/APICs a „Lowest Priority Arbitration“ is performed
  Goal: CPU that is currently processing the lowest priority task should handle the interrupt
    Respect Processor Priority Register und Task Priority Register
4.4 Advanced Programmable Interrupt Controller

## Slide 40: I/O-APIC
Nowadays typically integrated in the Southbridge of a PC chipset
24 interrupt inputs
  Cyclic querying done by the chip
Every interrupt input has a 64-bit entry in the Interrupt Redirection Table
  Describes the interrupt signal
  Determines the vector number and to which CPU core an interrupt is sent (used for generating the APIC bus message)
  Interrupt Redirection Table (IRT) has 24 entries
4.4 Advanced Programmable Interrupt Controller

## Slide 41: Interrupt Redirection Table Entry
4.4 Advanced Programmable Interrupt Controller
63:56 | Destination Field (R/W) | 8 bit target address → APIC ID (physical mode) or CPU group (logical mode)
55:17 | Reserved | 
16 | Interrupt Mask (R/W) | Enable/Disable interrupts
15 | Trigger Mode (R/W) | Edge/Level triggered interrupts
14 | Remote IRR (RO) | 
13 | Interrupt Pin Polarity (R/W) | Signal polarity
12 | Delivery Status (RO) | Interrupt message still in transit?
11 | Destination Mode (R/W) | Logical Mode or Physical Mode
10:8 | Delivery Mode (R/W) | 000 – Fixed → Deliver signal to all target processors 001 – Lowest Priority → Deliver to CPU with lowest priority task 010 – SMI → System Management Interrupt 100 – NMI → Non-Maskable Interrupt 101 – INIT → Initialize (reset) target CPU 111 – ExtINT → Answer to 8259A
7:0 | Interrupt Vector (R/W) | 8 bit vector number (16-254)